Typical Anchor Layout: 20’ by 40’ cable anchor dome, 4’ radius corners. Recommended anchors: Red Head brand, type J-38. Recommended Eyebolts: 3/8" diameter, standard thread, shortest shaft possible.

Dome-install-radiusx4

Typical Anchor Layout: 20’ by 40’ cable anchor dome, 2’ radius corners. Recommended anchors: Red Head brand, type J-38. Recommended Eyebolts: 3/8" diameter, standard thread, shortest shaft possible.

Dome-install-radiusx2

# Text boxes

Notes:

- First anchor from corner should be 4’-0” from corner.

- Distance between anchors not to exceed 3’-6’.

- Zipper should be centered between two anchors!!

- The close off (where the cable is spliced ) should also be centered between anchors to relieve stress at that point. This is very important in reducing strain on the zipper!!

Notes:

- First anchor from corner should be 2’-0” from corner.

- Distance between anchors not to exceed 3’-6”.

- Zipper should be centered between two anchors!!

This is very important on reducing strain on the zipper!!

- The close off (where the cable is spliced) should also be centered between anchors to relieve stress at that point.